## Slide 1: Construction Stormwater Best Management Practices
San Rafael, California November 12, 2015
Marin County Stormwater Pollution Prevention Program

## Slide 2: Disclaimer
The mention or image of any product or service is for illustrative purposes and is not an endorsement of the product or service.

## Slide 3: Basic principles of stormwater quality protection
Minimize pollutant exposure
  Don’t expose potential pollutants to wind and rain
Protect exposed pollutants
  Keep pollutants from being washed or blown away
Use and maintain Best Management Practices (BMPs)
  Procedures to minimize exposure or techniques to remove pollutants from runoff
Use BMPs in layers to protect water quality and plan for accidents
BMP Principles

## Slide 4: A few common sources of water pollutants on construction sites
Material | Pollutant | Effect on Creeks
Dirt and Dust | Sediment | Fills habitat, clogs gills, impairs ability to hunt
Concrete wastewater | pH | Toxic to aquatic life
Concrete wastewater Vehicle fueling & maintenance | Metals | Toxic to aquatic life
Paints and solvents | Synthetic organic compounds | Toxic to aquatic life
Landscape trimmings and fertilizers | Nutrients | Causes algal blooms, depletes oxygen
Landscape trimmings | Biochemical oxygen demand | Depletes oxygen
Asphalt/Paving Vehicle fueling & maintenance | Oil & grease | Causes sheen, toxic to aquatic life
BMP Principles

## Slide 5: Layers of BMPs
BMP Principles

## Slide 6: Connecting the dots between BMPs and activities
Construction Activities
Grading
Concrete
Trash
Clearing
Painting
Fueling
Landscaping materials
BMP Categories
Erosion Controls
Sediment Controls
Good Housekeeping
BMP Principles

## Slide 7: Erosion Control
Protects soil and prevents soil particles from becoming detached by rainfall, flowing water or wind
Soil protected as a resource
Source controls that prevent soil from becoming a pollutant
BMP Principles
Notes: Erosion control are the most important type of practices to prevent soil leaving a construction site.
When we start a construction project the initial work removes the existing soil cover – typically vegetation – sometimes hardscape. The clearing of the site, removes the protective cover that prevents erosion.
Soil can be eroded by wind blowing (wind erosion), rain drops hitting the soil (splash erosion), or by the force of water flowing over the surface (sheet and rill erosion).

## Slide 8: MCSTOPPP Minimum Control Measures
Erosion Controls
Scheduling
Protect existing vegetation
Creek set backs
Soil cover
Soil preparation/roughening
Erosion control blankets
Revegetation
BMP Principles

## Slide 9: Benefits of vegetation
BMP Principles

## Slide 10: Sediment Control
Practices that trap dirt particles – sediment – once they have been detached by rain, flowing water, or wind
  Various practices to slow and detain water to allow sediment to settle
  Treatment controls that remove soil from water or wind
BMP Principles
Notes: Sediment controls should be used as a back up for erosion controls.
These controls remove sediment particles from water or wind, but they are not very efficient or effective on a construction site.
The controls for the most part rely on slowing the water (or wind) down enough so that the particles can drop out by gravity. Some practices spread concentrated flows so they don’t create gullies.
They are ineffective because the sedimentation process takes a long time and or a lot of space. This is time and space we don’t have on a construction site.
Very few practices can filter sediment out of water. Most sediment particles are very small. Effective filters would pass water very slowly or clog and potentially cause flooding.

## Slide 11: MCSTOPPP Minimum Control Measures
Sediment Controls
Tracking controls
Fiber rolls (wattles)1
Silt fence1
Drain inlet protection
Trench dewatering
1Manufactured linear sediment controls
BMP Principles

## Slide 12: Good Housekeeping
Source control practices that minimize exposure of construction materials and waste to rain and wind
BMP Principles
Notes: These practices focus on all the other sources of pollutants at the construction site.
Use of spill containment systems, sheds and covers to keep rain from contacting materials or wastes, implementing procedures to ensure vehicles are serviced (in a way that doesn’t release pollutants), fuel storage practices …

## Slide 13: MCSTOPPP Minimum Control Measures
Good Housekeeping Practices
Concrete washout
Stockpile management
Hazardous material management
Sanitary waste management
Equipment and vehicle maintenance
Material storage
Litter and waste management
BMP Principles

## Slide 14: Erosion Control BMPs

## Slide 15: Scheduling
Integrate BMP implementation with activities
  Phase grading to limit amount of soil exposed
  Avoid grading during rainy periods
  Stabilize graded areas that become inactive
  Adjust activities based on predicted weather
  Re-vegetate during the appropriate growing conditions
  Comply with local winter work prohibitions
Erosion Control BMPs
Black Point Novato, Data Source UCCE
Notes: No it doesn’t mean you have a construction schedule!
Sequence and plan BMPs implementation based on weather and activities.
Some communities may prohibit work during the ‘rainy season’. Be forewarned that work in the winter, when we get most of our rain, BMPs will be more expensive.
Data in inches.

## Slide 16: Preserve vegetation and creek setbacks
Clear delineation
Ideally 25+ feet from creek (or as required by local ordinance)
Preserve existing vegetation in buffer
Install before construction starts
Erosion Control BMPs
Notes: Look for clear

## Slide 17: Preserve vegetation
Protect trees from construction
Establish protective zone around drip line of tree
Erosion Control BMPs

## Slide 18: Soil cover
Generic term for a variety of temporary BMPs that apply an erosion resistant cover to disturbed soil
  Straw mulch
  Hydraulic mulch
  Soil binders
  Wood mulch
  Compost blankets
  Non-vegetative stabilization
Erosion Control BMPs

## Slide 19: Track walked slope treated with hydromulch

## Slide 20: Slope treated with hydromulch

## Slide 21: Compost blankets
Pneumatic blower typically used to place compost
Roughen surface before application
1-4-inches thick
Seed can be incorporated
Slopes 2:1 or gentler
  Tackified on steeper slopes
Erosion Control BMPs

## Slide 22: Soil preparation and roughening
Soil Preparation includes raking, tilling, and incorporation of soil amendments to foster growth
  Typically part of the establishment of permanent vegetation
Soil Roughening includes track walking, stair stepping, decompacting soil to increase its resistance to erosion
  Employed for both temporary erosion control and permanent vegetation
  Used with soil cover and erosion control blankets

## Slide 23: Comparison of smooth and track walked slopes
Smooth compacted slope little opportunity for vegetation to take hold
Lots of pockets to catch water, soil, and seed
Notes: Reduction in erosion from track walked slopes (alone) 12-76%.

## Slide 24: Erosion control blankets
Anchor top to secure blanket and prevent undercutting
Install vertically downslope
Overlap (shingle) panels
Staple to secure to soil
Do not stretch blanket

## Slide 25: Wildlife friendly products
Avoid erosion and sediment control products that contain plastic nets (fixed aperture)
  Never use products that contain plastic nets for any BMP that will be part of the final stabilization
Use BMPs made of natural material without plastic nets

## Slide 27: Sediment Control

## Slide 28: Tracking control
A system of practices to minimize dirt from the project getting onto the roads and subsequently washed into storm drains
  Stabilized entrance
  Sweeping
  Access restrictions
    Limit access to stabilized entrance – no short cuts
    Limit access to necessary vehicles only
  Tire wash (optional, as needed)

## Slide 29: Stabilized entrance/exit
Size based on size of vehicles that will access site, bigger tires need longer entrances
  Typical BMP fact sheets are based on large trucks
Marin BMP adapted for smaller sites assuming light trucks would be the typical vehicle
  On smaller sites, install maximum length site can accommodate
  Install to allow two full rotations of tires on the entrance material
  Augment with rumble pads or racks
  Consider graveling access area/road
Sediment Control BMPs
Notes: Take entrance right

## Slide 30
Sediment Control BMPs
Rock
Rumble plate

## Slide 31
Sediment Control BMPs
Rock
Rumble plate
Gravel
Notes: Rock pad underlain with a geotextile fabric
  10 feet wide – accommodate width of vehicles
  16-20 feet long – accommodate two wheel rotations
  4-inch to 6-inch angular rock
  6 to 12 inches deep layer of rocks

## Slide 32: Fiber rolls (wattles) Type 1 installation
Install in shallow trench
Stakes through wattle hold wattle to the soil
Wattles with plastic nets must be removed.
Use for temporary sediment control only!
Notes: J-hook ends of roll uphill.
Stakes through wattle hold wattle to the soil
Plastic net – only for temporary installation. Must be removed!

## Slide 33: Fiber rolls (wattles) Type 2 installation
Notes: J-hook ends of roll uphill.
No trench needed, rope holds roll to soil.
All natural fibers can be left in place at the end of the project
Particularly good on slopes.
Good for long term installations – can be left in place.

## Slide 34
Notes: Fiber rolls must be staked to be effective. There are two proper method of installing fiber rolls. Neither involve the use of sand or gravel bags. If you cannot stake the wattles a different practice is needed. Several proprietary products have been developed for this type of installation. Dura wattle, Ertec Hard surface guard, shown here

## Slide 35: Silt fence – pay attention to the trench

## Slide 36: Tug test

## Slide 37: Drain inlet protection last line of defense
Protect drains on-site and immediately off-site
Use woven geotextile bag
  Resistant to photo degradation
Fill bags with washed gravel
  NOT SAND
  NOT DIRT
  NOT ASPHALT
Never use silt fence material to cover an inlet

## Slide 38: Setting up a treatment train to the drain
GRAVEL BAGS

## Slide 39: Storm drain inlet protection
J-hook check dam along the flow path
Protection at the drain

## Slide 40: Good Housekeeping

## Slide 41: Concrete washout
WashOut

## Slide 42: Stockpile management

## Slide 43: Hazardous materials management

## Slide 44: Sanitary facilities
… what is missing?
Secondary Containment Pans Stormwater Pollutant Protection

## Slide 45: Equipment and Vehicle Maintenance
Avoid conducting maintenance at the job site
Use drip pans, absorbent pads, and tarps to contain drips
Clean up small spills and drips immediately

## Slide 46: Waste and litter management

## Slide 47: Layers of BMPs
Erosion Control
Sediment Control
Good Housekeeping

## Slide 48
MCSTOPPP Minimum Control Measures
* Appendix in Applicant Package
48
Notes: We will spend more time later today discussing stormwater control measures or as they are more commonly known as Best Management Practices or BMPs.

## Slide 49
MCSTOPPP Trench Dewatering BMPs
*Appendix in Applicant Package
49
Notes: We will spend more time later today discussing stormwater control measures or as they are more commonly known as Best Management Practices or BMPs.

## Slide 50: Where to get more BMP info
CASQA California BMP Handbook, Construction
    www.casqa.org
Caltrans Stormwater Quality Handbook, Construction Site BMP Manual
    http://www.dot.ca.gov/hq/construc/stormwater/manuals.htm
Erosion and Sediment Control Field Manual
  San Francisco Bay Regional Water Quality Control Board (2002)
    Out of print

## Slide 51
Questions